Installation Notes

Need #1 Phillips (small) screwdriver, drill, 3/16" bit

Homeowner has two options: (1) Install new thermostat in place of the old one, unless the current thermostat is located in a place with unusual heating conditions (e.g., near stove, direct sunlight, fireplace, hot-water pipes) or unusual cooling conditions (e.g., draft from stairwell, door, or window); in a damp area such as a bathroom (this leads to corrosion); or in a place with poor air circulation (e.g., corner, alcove, behind door). (2) Pick a new location. If picking a new location, locate unit on an inside wall about 5 feet above the floor in an often-used room. However, wait to install until all work such as painting has been completed.

To avoid shock and damage to furnace, AC, and thermostat, power should be turned off at circuit breaker, fuse box, or appliance before installation begins. Remove the old thermostat’s cover: some covers snap on and pull off; others have locking screws on the side that must be loosened.

Wires must be labeled before they are removed. Use the labels that come packaged with the EC37. Letters (G, Y, W, RH, B, O, RC) will be printed near the terminals on the old unit. Label each wire as it is removed from the old unit’s terminal, making sure wires don’t fall back into hole in the wall. Then remove the old unit by loosening all the screws that attach it to the wall. Discard.

Prepare to install the EC37 by stripping insulation (about 3/8") from the wires coming out of the wall. This will clean off any corrosion. In addition, fill wall opening with nonflammable insulation. This will prevent drafts from affecting the unit. Separate the EC37’s body from the baseplate by pressing latch at bottom on the unit. New holes for the screws used to attach the baseplate to the wall might need to be drilled if mounting unit to soft material such as plasterboard. If so, drill 3/16" holes for each screw, and use the plastic anchors included in the package. Hold the base against the wall with the wires coming through the opening in the baseplate and attach to wall with the two screws included.

Attach the wires to the matching terminals (e.g., wire labeled G to terminal labeled G). Wires should not touch each other or other parts of the terminal. Make sure wires are trapped between black spacer and brass terminal. Tighten wires securely. Snap the unit’s body onto the baseplate.